SUMMARY OF RESEARCH PAPERS

3D Mapping with an RGB-D Camera
Felix Endres, Jürgen Hess, Jürgen Sturm, Daniel Cremers, Wolfram Burgard

In this paper, a 3D SLAM system for RGB-D sensors such as the Microsoft Kinect is presented. The approach uses two input images one RGB image and other is depth image. From color image geometric relationship between the landmarks and the bot position is extracted using techniques of SIFT and SURF and depth image is used to localize them in 3D. RANSAC is used to estimate the transformations between associated key points and optimize the pose graph using non-linear optimization. Beam based environment i.e EMM (environment measurement model) is used for reliable estimation that allows to evaluate the quality of a frame-to-frame estimate. There are limitations for this technique in large mam made environment because of similarity of obstacles.

2. Large-Scale Direct SLAM with Stereo Cameras
        Jakob Engel, J ̈org St ̈uckler, Daniel Cremers

A direct approach to SLAM with stereo cameras is presented in this paper. This method propose a
fixed-baseline stereo as well as temporal, variable-baseline stereo cues. Static image provide accurate depth within stereo range and temporal image depth is estimated that correspond to the translational motion between frames. This method aligns images using photometric and geometric residuals at a semi-dense set of pixels. Pixels are chosen where there is sufficient information for static or temporal stereo estimation. In future this technique is considered to be applied in multi camera setups and GPS systems.

3. An Evaluation of the RGB-D SLAM System
        Felix Endres1 Nikolas Engelha Daniel Cremers
        Jürgen Hessrd Jürgen Sturm Wolfram Burgard

In this paper the visual key points are exctracted from color image and uses depth image to localize them in 3D.RANSAC is used to estimate the transformations between RGBD frames and pose graoh is optimized. A volumetric 3D map of the environment is generated that can be used for robot localization, navigation , mapping and path planning.